## Slide 1
REST HOUSE, Bhokardan
Aurangabad division
GRIHA EB
4 STAR
: Bhokardan, Jalna district, Maharashtra
: 10,180 sq.m.
: 244 sq.m.
: Hospitality
: GRIHA for Existing Buildings (EB)
: 1
: 31 May 2019
: Government of Maharashtra
: Public Works Department (PWD) Maharashtra
: Built Environment (India) Pvt. Ltd
Location
Site Area
Built up Area
Typology
Rating Category
Version
Date of Award
Client
Integrated Design Team
Green Building Consultant
Total energy offset
by renewables
= 558.6%
Total reduction in
building water demand
= 6.3%
TOTAL CARBON OFFSET BY THE PROJECT:
By planting native saplings & preserving existing trees: 4.11 ton/year
By conservation of conventional energy: 8.20 ton/year
The following strategies were adopted by the project teams to
reduce the impact of the existing building on the environment:
Site Parameters:
Trees preserved on site in the ratio of 1 tree per 80 sq.m.
Preferred parking provided for electric vehicles
Strategies implemented over 8,194 sq.m. of site are to reduce the Urban Heat Island Effect.
Energy:
Replacing old electrical equipment and appliances with BEE star rated ones has reduced the annual energy consumption from 3,492 kWh/year to 783 kWh/year
Solar photovoltaic system proposed of 2 kWp to generate 3120 kWh of renewable energy.
Water Efficiency:
Building water consumption reduced from 250.025 kiloliters/year to 234.257 kiloliters/year
The total sewage water generated on site is 0.57 kiloliters/day.
Human Health and Comfort:
Indoor comfort conditions measured in summer months; Dry bulb temperature= 27 - 29°C, Relative humidity= 26% – 28%, Daylight levels= 152 - 195 lux, Artificial lighting levels= 102 - 191 lux and Indoor noise levels: 43 - 48 dB; were compliant with benchmarks of the Indian Model for Adaptive comfort, SP41 and NBC 2005.